## Slide 1
H
Harvard Robotics
MovieChat Memory for Long-Horizon Robot Policies
Can long-video memory compression transfer from QA to robot control?
Wenfei Yu
Harvard Robotics · July 2026
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
01

## Slide 2
Research Overview
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
02
01
Motivation & Research Question
Why long video memory may matter for RoboMME tasks
02
Prior Results & Gap
MovieChat works for QA; control may require a different interface
03
Method & System Design
OpenPI/pi0.5 with MovieChat, recurrent, and baseline variants
04
Experiments & Results
Initial results show modulation converges but underperforms
05
Next Steps
Test MovieChat memory as context tokens and inspect rollout failures

## Slide 3
01
Research Question
How should long-video memory condition diffusion-style robot policies?
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
03

## Slide 4
Why This Problem Matters
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
04
Long-horizon robot tasks require information that may only appear earlier in the video history.
01
CONTEXT
RoboMME includes reference and imitation tasks where the current frame is insufficient. The policy must preserve information from demonstrations, object states, and temporal goals.
RoboMME video-conditioned tasks
02
LIMITATION
MovieChat memory is designed for video QA, where a language model reads sparse visual evidence. A robot policy instead predicts denoising directions for future actions.
QA memory != action condition
03
OPPORTUNITY
If memory interface is the bottleneck, comparing context vs modulation can identify how long-video memory should enter embodied policies.
Memory interface ablation

## Slide 5
System Architecture
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
05
We evaluate whether compressed video memory improves OpenPI/pi0.5 action prediction on RoboMME.
PERCEPTION
FluxVLA SigLIP
front + wrist RGB -> 1152-d visual tokens
REPRESENTATION
MovieChat memory
short/long compression -> 128 memory tokens
POLICY
HistoryPi0 / OpenPI
memory + prompt + observation -> action chunk
CONTROL
Flow matching
noisy action + timestep -> denoising direction
ROBOT
RoboMME rollout
task success over 16 benchmark tasks
Compare memory as modulation vs context

## Slide 6
Quantitative Results
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
06
pi0.5 baseline
16.5%
80k checkpoint
Recurrent TTT
20.1%
best current result
MovieChat modul
8.9%
converged but weak
Context test
next
queued experiment
Success rate across RoboMME tasks
method variant
KEY TAKEAWAY
MovieChat memory is not automatically useful for control.
The modulation interface underperforms baseline despite stable training; memory-as-context is the next decisive test.
● Recurrent TTT ─ pi0.5 baseline ─ MovieChat modulation

## Slide 7
Qualitative Results
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
07
INITIAL STATE
INSTRUCTION
EXECUTION / ROLLOUT
RESULT
VideoPlaceOrder
“Watch the video, then place objects in the same order.”
demo frame
policy rollout
final state
MovieChat: partial success / unstable grounding
BinFill
“Fill the bin with the target object.”
initial scene
grasp attempt
bin approach
MovieChat below baseline
RouteStick
“Follow the demonstrated path with the stick.”
path cue
trajectory
collision / miss
memory not reliably used

## Slide 8
Ablations & Comparisons
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
08
Use this table to isolate whether the bottleneck is memory content or memory-policy interface.
METHOD / VARIANT
SUCCESS
TRAIN LOSS
INTERFACE
STATUS
pi0.5 baseline
16.5%
0.0049
none
completed
Recurrent TTT expert
20.1%
0.0048
expert / recurrent
completed
MovieChat modulation
8.9%
0.0090
modulation condition
completed
MovieChat context
pending
pending
prefix/context tokens
next experiment
Sidecar / online parity
diagnostic
n/a
encoder parity
planned
Token budget ablation
diagnostic
n/a
64 / 128 / 256
planned

## Slide 9
Conclusions & Future Work
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
09
CONCLUSIONS
✓
Recurrent TTT improves over pi0.5 baseline on RoboMME.
✓
MovieChat modulation trains stably but degrades rollout success.
✓
The key research variable is memory-policy interface, not just memory availability.
FUTURE WORK
Train MovieChat-context 80k · Evaluate by task family · Inspect rollout videos · Design action-aware retrieval
ROBOT

## Slide 10
Questions?
Main next test: MovieChat memory as readable context tokens for action policies.
Wenfei Yu · Harvard Robotics · RoboMME / OpenPI memory project
HARVARD ROBOTICS
RESEARCH PRESENTATION · 2026
10